THE PRINCIPAL  N. R. I. P. T. ALLAHABAD (U.P.)

Tender No.1/ Strenthening -2013						Date:-

ANNEXURE “A”

| SL.No. | Name of the Machine/Equipments with full Specification | Quantity |
| --- | --- | --- |
| 1. | PHOTO POLYMER PLATE MAKING EQUIPMENT Consist of Exposure Unit + washout unit + drier unit + UVC treatment unit, With Philips High intensity Lamp (with lamp cooling), Auto Temp Control, Reproduction should be less than 200 lpi 1% , Machine size 110X90X100cm, Crate Size 105X100X10cm. | 01 Nos. |
| 2. | PRINTING DOWN FRAME (AUTOMATIC) Exposing Area: 960X1200mm Light Source: 3Kw(Metal Halide Lamp) Pre vacuum exhausting, dual vacuum Microprocessor based electronic timer, light integrator for precise and accurate exposure | 01 Nos. |
| 3. | Book Sewing Machine The construction and the working of the machine at least speed of minimum 70 sections per minute, Largest size of book: 560x225 MM, Smallest size of book: 115x100 MM, NO. of stitches: UP to 9 Sets, Capacity: 70 SECTION/MIN | 01 Nos. |
| 4. | Perfect Binding Single Clamp Machine Clamping: Mechanical, Spine gluing: Three Roller, Side Gluing: Separate, Temp. Control: Digital, Spine length (Minimum):70-430mm, Spine Thickness (Minimum): 2mm-60mm, Speed 550 cycles/hour, Controls: Electro mechanical | 01 Nos. |
| 5. | 24" (600mm) Capacity 2 Colour Rotogravure Printing machine Model-600S2" with 6kw capacity heating chamber with 1HP high pressure blower, Manual rubber roll impression system with cylinder shaft & simplex unwind & rewind with mechanical shaft suitable for 76mm core ID can withstand 600mm dia roll with rell weight of 500kg, with 3HP main motor & 3HP rewind motor OPTIONAL ATTACHMENT : Unwind : Auto Tension Control Magnetic Powder Brake force cooled version, with tension controller, proximity and nos. load cells .Clutch controlled eddy current drive with load cells & its controls at rewind Web Aligner with its trolley with hydraulic power pack & its sensor on unwind unit. | 01 Nos. |
| 6. | 500mm Capacity 2 Colour Flexographic Printing Machine with 10" repeat size sterio rollers with 1 HP Hot air blower, with 200 mesh screen and anilox roller with 2 HP AC drive with its motor and control with mechanical brake at unwind & mechanical clutch at rewind with web guiding system at unwind with its power pack, sensor, hydraulic cylinder and digital tempreature controller with 1 HP blower, DOL inter locked, line speed 100mpm , with simplex unwind & rewind suitable for 76mm core ID & can withstand 00kg of reel weight,with auto tension controle unit. | 01 Nos. |
| 7. | Semi automatic Screen Printing m/c with stainless steel vacuum bed Print area : 15”x20” (38.1 x 50.8 cm) Max Substrate thickness : 5to7 mm., Micro registration system :±0.01 mm (with allied equipments, exposure unit, coating unit,pneumatic stretching unit and retouching table) | 01 Nos. |